## Slide 1: Socket Communication Using AT+QIOPEN and AT+QISEND
Reuben Mathew

## Slide 2: What is Socket Communication?
Socket communication allows an IoT module to establish a TCP/IP or UDP/IP connection to a remote server.
Used for sending/receiving data over the internet (e.g., to APIs, MQTT brokers).
It's crucial for applications like remote monitoring, data logging, and cloud-connected devices.

## Slide 3: Cavli Modules Supporting TCP/IP
Cavli modules that support socket communication (via Quectel-compatible commands):
- C10QS (LTE Cat NB1/eMTC)
- C42QM (LTE Cat 1)
- C16QS (GSM/GPRS)
These modules support Quectel-style AT commands like AT+QIOPEN and AT+QISEND.

## Slide 4: AT+QIOPEN – Open a Socket Connection
Used to open a TCP or UDP socket on the module.
Syntax:
AT+QIOPEN=<ctxid>,<connectID>,"<service_type>","<IP/domain>",<port>,<mode>
Example:
AT+QIOPEN=1,0,"TCP","142.250.195.78",80,0
Response:
+QIOPEN: 0,0 (0 = success)

## Slide 5: AT+QISEND – Send Data Over Socket
Used to send data through an open socket connection.
Syntax:
AT+QISEND=<connectID>,<length>
Example:
AT+QISEND=0,18
> Hello from Cavli!
[Ctrl+Z]
Response: SEND OK

## Slide 6: Socket Communication Flow
1. Configure PDP context (e.g., AT+CGDCONT=1,"IP","<APN>")
2. Activate PDP context: AT+CGACT=1,1
3. Open socket: AT+QIOPEN=1,0,"TCP","<server>",<port>,0
4. Wait for: +QIOPEN: 0,0
5. Send data: AT+QISEND=0,<length>
6. Close socket (optional): AT+QICLOSE=0

## Slide 7: Response Codes & Troubleshooting
Common response codes for AT+QIOPEN:
- +QIOPEN: <id>,0 → Success
- +QIOPEN: <id>,565 → Connection failed (e.g., unreachable server)
AT+QISEND Issues:
- SEND FAIL: Socket not open or unstable connection
- Solution: Check network, PDP context, and server address

## Slide 8: Conclusion
AT+QIOPEN and AT+QISEND are vital for implementing socket communication in Cavli's IoT modules.
They enable sending data to remote servers using TCP/IP protocols, essential for cloud-enabled applications.
Though not supported in CelerSMS Emulator, understanding these commands is key for working with real modules.